## Slide 1
TensPilot+
Design of a Dual-Mode TENS Device
with a Companion Web Application

## Slide 2
Presentation Outline
• The Problem & Our Solution
• Hardware Design & Specifications
• Testing & Clinical Results
• Two Therapy Modes
• Software Ecosystem (Patient App & Doctor Dashboard)
• AI Integration (Gemini)
• Innovation & Key Features
• Impact & SDGs

## Slide 3
1. The Problem & Our Solution
The Problem
• Standard TENS machines are standalone systems.
• No tracking of pulse width, frequency, or intensity.
• Reliance on unreliable paper diaries.
• Doctors have limited visibility into home therapy.
Our Solution
A low-cost, locally developed TENS device integrated with an intelligent monitoring platform to bridge the gap between home and hospital.

## Slide 4
2. Hardware Design
HARDWARE PHOTO
(Device showing
LCD display, controls & layout)
Specifications
• Arduino Uno (ATmega328P)
• L298N H-Bridge driver
• XL6009 Boost converter
• 20x4 LCD display
• 5V Power Bank
• Size: 150×100×56 mm
• Weight: ~350g
• Battery: 4+ hours

## Slide 5
3. Testing & Results
VOLUNTEER
TESTING PHOTO
(Device on
forearm, electrodes placed)
Results from 12 Volunteers
• Signal accuracy: ±2%
• Charge balance: >98%
• Frequency range: 1–120 Hz stable
• Battery life: 4+ hours continuous
• Conventional mode: smooth tingling
• Acupuncture mode: rhythmic tapping
• No adverse effects reported
• Safe electrical parameters

## Slide 6
4. Two Therapy Modes
CONVENTIONAL MODE
20–120 Hz
Fast pain relief (10–20 minutes)
For acute pain & muscle soreness
Smooth tingling sensation
ACUPUNCTURE-LIKE MODE
1–10 Hz
Longer relief (90–180 minutes)
For chronic & neuropathic pain
Rhythmic tapping with contractions

## Slide 7
5. Ecosystem: Patient Application
Home & Setup
Screenshot
Active Session
Screenshot
Session History
Screenshot
App Features
• Intuitive Setup
• Live Logging
• Pain Tracking Algorithm
• Offline Access (PWA)

## Slide 8
6. Ecosystem: Doctor Dashboard
Main Dashboard View
(Total Patients, Pain Stats,
Weekly Activity)
Patient Invite
Modal Code
Clinical Oversight
• Remote Session Tracking
• Patient Compliance Analytics
• Generate Invite Codes
• Real-Time Progress Charts

## Slide 9
7. AI Integration: Gemini Virtual Assistant
AI Chat
Screenshot
Gemini Capabilities
• Recommends electrode placement based on pain type.
• Provides therapy guidance 24/7.
Key Benefits
• Reduces patient misinformation.
• Improves therapy adherence.

## Slide 10
8. Innovation & Key Features
Hardware
• Dual-mode capability
• Arduino-based
• Open-source design
• 20–30% cheaper
Software
• Progressive Web App
• Offline-first (no internet)
• Local data storage
• Privacy-focused
Integration
• Manual data entry (current)
• Session tracking
• Progress analytics
• Future: Bluetooth

## Slide 11
9. Impact, Accessibility & SDGs
Designed for Nigeria
✅ Works Offline via Service Workers
✅ Runs on low-end Android phones
✅ Reduces transportation costs
✅ Targets Vulnerable Demographics (Women, Elderly, Children)
Addressing SDGs
• SDG 3: Good Health & Well-being
• SDG 9: Industry & Innovation
• SDG 10: Reduced Inequalities
• SDG 17: Partnerships for the Goals

## Slide 12
Thank You For Listening!
TensPilot+
Any Questions?